## Slide 1: Meteoroid Ejecta of Lunar Secondaries Engineering Model
Anthony M. DeStefano
NASA/MSFC/EV44 Natural Environments
Applied Space Environments Conference 2021

## Slide 2: Outline
A Typical Meteoroid Ejecta Model Algorithm
Current Meteoroid Ejecta Environment – NASA SP-8013
Updated Model – Meteoroid Ejecta of Lunar Secondaries Engineering Model (MELSEM)
  Primary Environments
  Asset Geometry and Location
  Scaling Laws
  Secondary Environment at Asset
Risk Assessment – Probability of No Penetration

## Slide 3: Typical Meteoroid Ejecta Model Algorithm
What are the primary impactors?
  Cumulative flux as a function of impactor mass
  Impactor density
  Possibly angular and location-dependent information
How to convert primary mass flux into ejected mass flux?
  Scaling laws – extrapolations from laboratory experiments and/or theory
How is the ejected mass flux distributed – starting from primary impact location?
  Solid angle
  Particle size and density
  Speed
For a given observer, what is the total ejected mass flux, accounting for impacts over the entire surface of the Moon?
  Solid angle
  Particle size and density
  Speed

## Slide 4: NASA SP-8013 – Lunar Ejecta Environment
The Cross-Program Design Specification for Natural Environments (DSNE) rev. H, Section 3.4.8.2 points to NASA SP-8013, Section 3.2 for the Meteoroid Ejecta Environment
  Power-law expressions are given for various ejecta speed ranges of the cumulative flux as a function of ejecta particle mass
  A single particle density is assumed at 2.5 g/cm3

## Slide 5: NASA SP-8013 – Lunar Ejecta Environment
NASA SP-8013 is consistent with Grun et al. 1985
  Grun et al. 1985 is used to scale the Meteoroid Engineering Model (MEM) for primary sizes of 1 ug to 10 g
Scaling laws implied from NASA SP-8013 from Zook 1967

## Slide 6: Sporadic meteoroid flux (low and high density populations in MEM)
Moorhead 2019
Apex & toroidal
Helion/antihelion
Log-normal distributions

## Slide 7: Lunar Surface Ephemeris for MEM – JPL Horizons
A total of 148 ephemeris files generated for a fixed location on the Moon
  19-year (Metonic cycle) time period of trajectory
  5-degree latitude intervals from south pole to north pole
  90-degree longitude intervals
  Timestep ~ 16 hours 40 minutes (10,000 total)

## Slide 8: Sporadic meteoroid flux (angle/speed) and latitudinal dependence on the lunar surface

## Slide 9
Sporadic meteoroid flux (alt/az) and latitudinal dependence on the lunar surface

## Slide 10: Near Earth Object (NEO) flux (Brown et al. 2002) at the lunar surface
Moorhead (see memo OSMA/MEO/Lunar-001) computed the NEO flux at the lunar surface based on Brown et al. 2002 and velocity distribution of bolides reported by the Center for Near Earth Object Studies (CNEOS)
In MELSEM, we approximate the angular distribution of fluxes at the lunar surface by the low-density population of MEM

## Slide 11: Asset Geometry and Location
The asset, or observer, is the physical object at which the meteoroid ejecta is collected from all impacts over the entire surface of the Moon to generate the meteoroid ejecta environment
  Typical simplifying shapes of the object include:
    Sphere
    Cylinder
    Rectangular Prism
  The asset can be made of any number of these shapes, but for simplicity, a cylinder is often chosen for the lunar lander
  The location of the asset can be on the lunar surface or any distance above the lunar surface
    In general, a full trajectory could be used, but a single-point location is used for simplicity

## Slide 12: Impact-ejecta scaling model (Housen & Holsapple 2011)
  where and for sand fly ash (porosity of 45%)
  is the regolith particle density, see DSNE
  is the projectile particle (primaries) density, which can be integrated out over the density distribution from MEM
  is the primary mass, which can also be integrated out over the Grun differential flux
  is the normal component of the projectile speed (speed and impact angle taken from MEM)

## Slide 13: Differential ejecta flux vs. distance
Various cylindrical lander heights were simulated using Monte Carlo for various impact distances
  For simplicity, these simulations used 2D due to the symmetry – off radial hits assumed to have same width as radial width (conservative)
Orbits solved using RKF45 integration of equations of motion (variable time stepping):
MC sims show:
  and , very close to the analytic estimates!
The c parameter is related to the distance scale () at which the height of the lander is not driving the ejecta flux
*Assuming isotropic ejecta with a speed distribution

## Slide 14: Integral ejecta flux vs. Impact distance
, the integral ejecta flux as a function of impact distance
, the differential ejecta flux as a function of distance
From analytic results, we expect:
  , and
  Due to the speed distribution
Impact Distance (from lander edge) (m)
Integral ejecta flux (fraction of ejecta flux > d_I)
1: h=7m
2: h=11m
3: h=50m

## Slide 15: Effects of minimum ejecta speed on differential ejecta flux
Imposing a minimum ejecta speed eliminates the bulk of the ejecta at close distances
  Low-energy ejecta (speed and mass) may be irrelevant to the impact risk
Further distances are not affected by a minimum speed cut-off
  Not enough speed to reach far distances in the first place

## Slide 16: Differential flux (solid-marked) and integral flux (dashed) vs. min speed cut-off
Integral flux is flux of ejecta from distances d and further, for all speeds greater than vmin
E.g., 86.5% of the ejecta hitting the lander is < 100 m/s
*Assuming isotropic ejecta with a speed distribution