## Slide 1: Lunar Meteoroid Ejecta Model
Anthony M. DeStefano
NASA/MSFC/EV44 Natural Environments
11/17/2020

## Slide 2: Overview
Results of LuMEM
  Igloo number flux distribution (based on MEM3, see Moorhead et al 2019)
  Example DSNE Table for Rev. I
  HVIT Probability of No Penetration (PNP) Comparison
DSNE Rev H Lunar Ejecta Model – NASA SP-8013 (1969)
  Based on Zook 1967
Brief (non-exhaustive) Review of Impact-Ejecta Scaling Models
  Zook 1967
  Krivov et al. 2003
  Housen & Holsapple 2011
Proposed New DSNE Model -- Lunar Meteoroid Ejecta Model (LuMEM)
  Sporadic meteoroid flux (Grun et al 1985)
  Near Earth Object (NEO) flux (Brown et al 2002)
  Impact-ejecta scaling model (Housen & Holsapple 2011)
  Ejecta particle size distribution (Carrier 2003)
  Ejecta zenith angle distribution (empirically from Gault & Wedekind 1978)
  Ejecta azimuth angle distribution (modified from Rival & Mandeville 1999)
Analytic model of lunar ejecta
  Speed distribution as a function of distance
  Secondary flux as a function of distance
  Secondary flux in terms of primary flux

## Slide 3: Example DSNE Table for Rev. I
The speed bins 0.1-0.3 km/s, 0.3-1 km/s, and 1-2.4 km/s were suggested by the HVIT who run Bumper for probability-of-no-penetration (PNP) risk analysis
  The corresponding speed bin centers (weighted by the speed distribution and the energy) are 170 m/s, 535 m/s, and 1530 m/s.
At this point, we are assuming an isotropic azimuth ejecta environment and are only showing the impact angle dependency
  SP-8013 and other models do not include angular dependency at all
  The angular dependency may be important for long-term structure on the lunar surface
The HVIT has worked with us to verify correct interpretation of our environment in the Bumper code
Preliminary

## Slide 4: Results from the Lunar Meteoroid Ejecta Model (LuMEM)
The LuMEM produces igloo fluxes (alt/az/speed) in the same format as MEM
  External models (e.g., Bumper) that use MEM files can also use our LuMEM environments
The particle size distribution is assumed to be the same as the lunar regolith (Carrier 2003)
The speed distribution follows power-law scaling (Housen & Holsapple 2011) that depends implicitly on the lunar regolith properties (e.g., porosity)

## Slide 5: HVIT Probability of No Penetration (PNP) Comparison
HVIT compared the primary MEM environment (low & high density populations) with the SP-8013 and LuMEM (called DLE in the table) ejecta environments
  Preliminary results show that LuMEM is:
  at worst 3.6 times less risk than MEM
  at worst 20.4 times less risk than SP-8013
Preliminary

## Slide 6
Downstream
MEM Low Density Population
MEM High Density Population
Near Earth Object Population
Ejecta Angular Distribution (for 45 degree impact)
Total Ejecta Angular Distribution (at 45 degrees latitude)

## Slide 7: Forward Work
Compute NEO angular distribution from NEO orbital elements
Plans to provide lunar ejecta environment for meteor showers (only the sporadic meteors are considered in MEM
Ability to compute lunar ejecta environment for short-term mission profiles at specific longitude/latitude locations on the Moon
If there is interest, modifications to the code could be made to compute ejecta environments for a particular orbit around the Moon (such as at Gateway)

## Slide 8: Overview
Results of LuMEM
  Igloo number flux distribution (based on MEM3, see Moorhead et al 2019)
  Example DSNE Table for Rev. I
  HVIT Probability of No Penetration (PNP) Comparison
DSNE Rev H Lunar Ejecta Model – NASA SP-8013 (1969)
  Based on Zook 1967
Brief (non-exhaustive) Review of Impact-Ejecta Scaling Models
  Zook 1967
  Krivov et al. 2003
  Housen & Holsapple 2011
Proposed New DSNE Model -- Lunar Meteoroid Ejecta Model (LuMEM)
  Sporadic meteoroid flux (Grun et al 1985)
  Near Earth Object (NEO) flux (Brown et al 2002)
  Impact-ejecta scaling model (Housen & Holsapple 2011)
  Ejecta particle size distribution (Carrier 2003)
  Ejecta zenith angle distribution (empirically from Gault & Wedekind 1978)
  Ejecta azimuth angle distribution (modified from Rival & Mandeville 1999)
Analytic model of lunar ejecta
  Speed distribution as a function of distance
  Secondary flux as a function of distance
  Secondary flux in terms of primary flux

## Slide 9: DSNE Rev H Lunar Ejecta Model NASA SP-8013 (1969)
Average speed [both] = 20 km/s
Density [NASA SP-8013] = 0.5 g/cm^3
Density [Grun et al 1985] = 2.5 g/cm^3
Density = 2.5 g/cm^3

## Slide 10: Overview
Results of LuMEM
  Igloo number flux distribution (based on MEM3, see Moorhead et al 2019)
  Example DSNE Table for Rev. I
  HVIT Probability of No Penetration (PNP) Comparison
DSNE Rev H Lunar Ejecta Model – NASA SP-8013 (1969)
  Based on Zook 1967
Brief (non-exhaustive) Review of Impact-Ejecta Scaling Models
  Zook 1967
  Krivov et al. 2003
  Housen & Holsapple 2011
Proposed New DSNE Model -- Lunar Meteoroid Ejecta Model (LuMEM)
  Sporadic meteoroid flux (Grun et al 1985)
  Near Earth Object (NEO) flux (Brown et al 2002)
  Impact-ejecta scaling model (Housen & Holsapple 2011)
  Ejecta particle size distribution (Carrier 2003)
  Ejecta zenith angle distribution (empirically from Gault & Wedekind 1978)
  Ejecta azimuth angle distribution (modified from Rival & Mandeville 1999)
Analytic model of lunar ejecta
  Speed distribution as a function of distance
  Secondary flux as a function of distance
  Secondary flux in terms of primary flux

## Slide 11: Impact-Ejecta Scaling Models Zook 1967
  Where for km/s
  The index is the power-law index of
  the primary flux curve (see previous slide)
  The parameter ranges from 0.3-0.7 (Zook ‘67)
    In general, (Gault et al. 1963), property of
    the target material
Implicitly, , which defines
as a function of and

## Slide 12: Impact-Ejecta Scaling Models Krivov et al. 2003
  is the power-law exponent to the crater volume vs. impact kinetic energy
    Figure 7 of Koschny & Grun 2001 show for ice-silicate targets
    Moore et al. 1963 give for basalt targets
  is the ejecta mass distribution (CDF) slope (akin to our analysis of Carrier 2003)
    Plausible slopes range from 0.5 to 1 (see Krivov & Jurewicz 1999)
    The most likely slope is ~0.8 (see Krivov et al. 2000)
      Note: corresponds to < 7E-5 g particles if using Carrier 2003
  is the speed CDF slope
    is for hard-surface targets, and is for regolith-like targets (i.e., porous) (see Krivov et al. 2003)

## Slide 13: Impact-Ejecta Scaling Models Housen & Holsapple 2011
  and are determined by the target properties. For all cases studied, , see Housen & Holsapple 2011
  The ejecta mass CDF term is derived from Carrier 2003, where the small and large scale ejecta mass is compared with for a regolith particle density g/cc

## Slide 14: Overview
Results of LuMEM
  Igloo number flux distribution (based on MEM3, see Moorhead et al 2019)
  Example DSNE Table for Rev. I
  HVIT Probability of No Penetration (PNP) Comparison
DSNE Rev H Lunar Ejecta Model – NASA SP-8013 (1969)
  Based on Zook 1967
Brief (non-exhaustive) Review of Impact-Ejecta Scaling Models
  Zook 1967
  Krivov et al. 2003
  Housen & Holsapple 2011
Proposed New DSNE Model -- Lunar Meteoroid Ejecta Model (LuMEM)
  Sporadic meteoroid flux (Grun et al 1985)
  Near Earth Object (NEO) flux (Brown et al 2002)
  Impact-ejecta scaling model (Housen & Holsapple 2011)
  Ejecta particle size distribution (Carrier 2003)
  Ejecta zenith angle distribution (empirically from Gault & Wedekind 1978)
  Ejecta azimuth angle distribution (modified from Rival & Mandeville 1999)
Analytic model of lunar ejecta
  Speed distribution as a function of distance
  Secondary flux as a function of distance
  Secondary flux in terms of primary flux

## Slide 15: Sporadic meteoroid flux (Grun et al. 1985)
MEM3 is valid for interplanetary fluxes with masses greater than 1E-6 grams
  The Grun flux in this case is normalized to 1 at 1E-6 grams
The Grun fluxes [#/m^2/yr] in the range 1E-6 to 10 grams can be fit by a double power-law
When accounting for all primary masses, the differential Grun flux [#/m^2/yr/g] is integrated over with the mass dependence of the particular scaling law

## Slide 16: Sporadic meteoroid flux (low and high density populations in MEM)
Moorhead 2019
Apex & toroidal
Helion/antihelion
Log-normal distributions

## Slide 17: Lunar Surface Ephemeris for MEM – JPL Horizons
A total of 37 ephemeris files generated for a fixed location on the Moon
  19-year (Metonic cycle) time period of trajectory
  5 degree latitude intervals from south pole to north pole
  0 degrees longitude (central meridian)
  Timestep ~ 16 hours 40 minutes (10,000 total)

## Slide 18: Sporadic meteoroid flux (angle/speed) and latitudinal dependence on the lunar surface

## Slide 19
Sporadic meteoroid flux (alt/az) and latitudinal dependence on the lunar surface

## Slide 20: Near Earth Object (NEO) flux (Brown et al. 2002) at the lunar surface
Althea Moorhead (see memo OSMA/MEO/Lunar-001) computed the NEO flux at the lunar surface based on Brown et al. 2002 and velocity distribution of bolides reported by the Center for Near Earth Object Studies (CNEOS)
In LuMEM, we approximate the angular distribution of fluxes at the lunar surface by the high density population of MEM
  The high density population in MEM comes from the equatorial plane, “similar to the NEOs”

## Slide 21
NEO flux and latitudinal dependence on the lunar surface

## Slide 22: Impact-ejecta scaling model (Housen & Holsapple 2011)
  where and for sand fly ash (porosity of 45%)
  is the regolith particle density, see DSNE
  is the projectile particle (primaries) density, which can be integrated out over the density distribution from MEM
  is the primary mass, which can also be integrated out over the Grun differential flux
  is the normal component of the projectile speed (speed and impact angle taken from MEM)

## Slide 23: Trajectory and spherical geometry of secondary ejecta
Orbital mechanics
Impact and ROI distance from lunar surface the same (trajectory is symmetric about the apoapsis/periapsis)
Visual aid to guide intuition – converting ejecta at impact location to ejecta collected at Region-of-Interest

## Slide 24: Integrating arbitrary domain – Step 1
Recursively break down the domain to find regions between the two curves
  i.e., Search for ejecta angle/speed pairs that reach the ROI
Ejecta Speed
Ejecta Zenith Angle

## Slide 25: Integrating arbitrary domain – Step 1
Recursively break down the domain to find regions between the two curves
  i.e., Search for ejecta angle/speed pairs that reach the ROI
Ejecta Speed
Ejecta Zenith Angle

## Slide 26: Integrating arbitrary domain – Step 1
Recursively break down the domain to find regions between the two curves
  i.e., Search for ejecta angle/speed pairs that reach the ROI
Red regions are completely outside of the domain
Yellow regions are partially in the domain
Green regions are completely inside the domain
Ejecta Speed
Ejecta Zenith Angle

## Slide 27: Integrating arbitrary domain – Step 2
Recursively break down yellow regions partially in the domain
  i.e., Search for ejecta angle/speed pairs that reach the ROI
Red dots are completely outside of the domain
Green dots are completely inside the domain
Ejecta Speed
Ejecta Zenith Angle

## Slide 28: Integrating arbitrary domain – Step 2
Recursively break down yellow regions partially in the domain
  i.e., Search for ejecta angle/speed pairs that reach the ROI
Red dots are completely outside of the domain
Green dots are completely inside the domain
  Only green dots are where the integral is evaluated
Ejecta Speed
Ejecta Zenith Angle

## Slide 29: Ejecta particle size distribution (Carrier 2003)
Carrier 2003 gives the cumulative particle size distribution normalized by mass and not particle number
  To convert to particle number, we need to evaluate the integral:
  It can be shown that the cumulative particle size distribution normalized by number is (x in mm):
  Note that SP-8013 gives:
Size range of LADEE/LDEX observations (0.1 – 5 um, Horanyi et al. 2014)
-- They show in this regime (Horanyi et al. 2015)

## Slide 30: Ejecta zenith angle distribution (empirically from Gault & Wedekind 1978)
The maximum ejecta zenith angle as a function of ejecta azimuth from the down stream direction of the primary impact:
Zenith angle distribution (formally, a beta distribution in cosine of the zenith angle):
Defined so that α_max is the peak of the distribution

## Slide 31: Ejecta azimuth angle distribution (modified from Rival & Mandeville 1999)
The azimuth distribution is defined so that the downstream direction is preferred if the impact zenith angle is not normal
If there is a normal impact, the azimuth distribution is isotropic
For oblique impacts (greater than 70 degrees), the azimuth distribution begins to have an exclusion zone in the upstream direction, defined by

## Slide 32: Ejecta full angular distribution

## Slide 33: Backup

## Slide 34: Overview
Results of LuMEM
  Igloo number flux distribution (based on MEM3, see Moorhead et al 2019)
  Example DSNE Table for Rev. I
  HVIT Probability of No Penetration (PNP) Comparison
DSNE Rev H Lunar Ejecta Model – NASA SP-8013 (1969)
  Based on Zook 1967
Brief (non-exhaustive) Review of Impact-Ejecta Scaling Models
  Zook 1967
  Krivov et al. 2003
  Housen & Holsapple 2011
Proposed New DSNE Model -- Lunar Meteoroid Ejecta Model (LuMEM)
  Sporadic meteoroid flux (Grun et al 1985)
  Near Earth Object (NEO) flux (Brown et al 2002)
  Impact-ejecta scaling model (Housen & Holsapple 2011)
  Ejecta particle size distribution (Carrier 2003)
  Ejecta zenith angle distribution (empirically from Gault & Wedekind 1978)
  Ejecta azimuth angle distribution (modified from Rival & Mandeville 1999)
Analytic model of lunar ejecta
  Speed distribution as a function of distance
  Secondary flux as a function of distance
  Secondary flux in terms of primary flux

## Slide 35: Speed distribution as a function of distance
Differential area
Azimuthal field-of-view
Ejecta speed distribution
Geometric factor

## Slide 36: Distance distribution as a function of speed
For speeds less than sqrt(2)/2 (or < 0.7071 * v_esc)
  A very specific distance (a ring around the ROI) contributes to a given ejecta speed
For speeds greater than 0.7071 * v_esc and less than ~0.9 * v_esc
  A range of distances from ~0.35 to 0.6 * circumference of Moon (like a hemispherical cap centered at the antipode) contribute to a given ejecta speed
For speeds greater than ~0.9 * v_esc
  Distances greater than ~0.4 * circumference of Moon, which is the entire Moon contributes to a given speed
Each integral over the distance for each speed gives a weight of 1

## Slide 37: Secondary flux as a function of distance
The ejecta speed distribution as a function of distance from primary impact point follows a power-law for all distances
  We see that the secondary fluxes are dominated by impacts that are close by (when taking into account the power-law speed distribution from Housen & Holsapple 2011)
  There is a correction factor to the power-law relation that only varies by about 10% over the whole Moon for (the antipodal location is underestimated, which is a minor contribution to the over flux)

## Slide 38: Secondary flux from impacts over the whole Moon in terms of secondary flux from a single impact on the Moon
Secondary flux as a function of ejected angle from zenith
Secondary flux if all ejecta is ejected at 45 degrees
Secondary flux assuming isotopically ejected ejecta, shown to be comparable to ejecta only at 45 degrees
  E.g., if v_min = 100 m/s, then the size of the ROI must be << 5.2 meters, otherwise higher terms come into play
From HH11 scaling laws